## Slide 1: DAIDALUS Analysis Tools
Jason Davies (ARC-AFT)[USRA]
November 13, 2017

## Slide 2: Background
Desired an easy-to-use toolchain for working DAIDALUS with flight-test data
MATLAB environment is great for data analysis tasks
Designed to work with ACAS-Xu FT2 LVC/GPS logs
  Standard data types are portable to other analysis scenarios

## Slide 3: Common Data Structures
LVC Messaging
Aircraft States
DAIDALUS Bands
DAIDALUS Alerts

## Slide 4: LVC Messaging
messages [struct]: Formatted LVC messages
  .Name: Message Type
  .Data: Data Payload
  .time: Time of Applicability
Notes: messages [struct]: Formatted LVC messages
  .Name: Message Type
  .Data: Data Payload
  .time: Time of Applicability

## Slide 5: LVC Messaging
LVC Messages Structure
.Name
.Data
.time
Mixed LVC Message Types
getLVC()
LVC Log File
.csv

## Slide 6: Aircraft States (trafficState)
trafficState [struct]: Aircraft Traffic State
  .Name: Aircraft callsign
  .UID: Unique Identifier
  .lat: latitude
  .lon: longitude
  .alt: Altitude
  .track: Track/heading
  .gs: Ground speed
  .vx: latitude velocity
  .vy: longitude velocity
  .vz: climb rate
  .time: time UTC

## Slide 7: Aircraft States (trafficState)
getTrafficState*()
Aircraft trafficState
.Name
.UID…
States of Ownship and Intruder(s)
Ikhana/N3GC GPS Log
.csv
LVC Messages
.Name
.Data
.Time
genScenarioLVC()
Encounter File
.daa
getTrafficStateDAA()
GPS
LVC
Encounter File

## Slide 8: DAIDALUS Bands
*Bands [struct]: DAIDALUS Bands in a given dimension
.time: Timestep
.NONE: NONE level segment
.FAR: FAR segment
.MID: MID segment
.NEAR: NEAR segment
.RECOVERY: RECOVERY segment
.bands_drawn: any(Bands > NONE)
.timeToRecovery: Time to recovery
Notes: *Bands [struct]: DAIDALUS Bands in a given dimension
  .time: Timestep
  .NONE: NONE level segment
  .FAR: FAR segment
  .MID: MID segment
  .NEAR: NEAR segment
  .RECOVERY: RECOVERY segment
  .bands_drawn: Any Bands > NONE?
  .timeToRecovery: Time to recovery

## Slide 9: DAIDALUS Bands
*Bands
.Time
.NONE
.FAR…
States of Ownship and Intruder(s)
Encounter File
.daa
getDAIDBands()
DAIDALUS Configuration
.txt

## Slide 10: DAIDALUS Alerts
Alert Level
Alerting Timelines
Separation Statistics
Projected State Statistics
Alerts[struct]: DAIDALUS Alerts for each intruder

## Slide 11: DAIDALUS Alerts
Alerts
.Time
.Ownship
.Traffic…
States of Ownship and Intruder(s)
Encounter File
.daa
getDAIDAlerts()
DAIDALUS Configuration
.txt
Units
.Time
.Ownship
.Traffic…

## Slide 12: Goals
Generate DAIDALUS inputs
Generate DAIDALUS outputs
Visualize guidance and encounter geometry
Plot DAIDALUS outputs for in-depth analysis

## Slide 13: Goals
Generate DAIDALUS inputs
Generate DAIDALUS outputs
Visualize guidance and encounter geometry
Plot DAIDALUS outputs for in-depth analysis

## Slide 14: Generate DAIDALUS inputs
DAIDALUS Inputs
Aircraft States
ADS-B GPS
Encounter File
.daa
Encounter File
.daa
DAIDALUS Configuration
.txt

## Slide 15: Generate DAIDALUS inputs: Encounter Files
Encounter File .daa
LVC Messages
.Name
.Data
.Time
Aircraft trafficState
.Name
.UID…
Aircraft trafficState
.Name
.UID…
genScenarioLVC()
genScenarioTrafficState()

## Slide 16: Goals
Generate DAIDALUS inputs
Generate DAIDALUS outputs
Visualize guidance and encounter geometry
Plot DAIDALUS outputs for in-depth analysis

## Slide 17: Generate DAIDALUS Outputs
DAIDALUS Outputs
DAIDALUS Inputs
Alerts
.Time
.Ownship
.Traffic…
Encounter File
.daa
Units
.Time
.Ownship
.Traffic…
DAIDALUS Configuration
.txt
getDAIDBands()
*Bands
.Time
.NONE
.FAR…
getDAIDAlerts()

## Slide 18: Goals
Generate DAIDALUS inputs
Generate DAIDALUS outputs
Visualize guidance and encounter geometry
Plot DAIDALUS outputs for in-depth analysis

## Slide 19
DAIDALUS Guidance Visualization:
Bands visualization in all 4 dimensions
2D visualization of encounter
Alert levels per intruder
Produces portable .avi video file
drawBandsDAIDALUS()

## Slide 20
drawBandsDAIDALUS()
Aircraft trafficState
.Name
.UID…
Alerts
.Time
.Ownship
.Traffic…
Units
.Time
.Ownship
.Traffic…
*Bands
.Time
.NONE
.FAR…
DAIDALUS Configuration
.txt
Encounter.avi
DAIDALUS Guidance Visualization:
drawBandsDAIDALUS()

## Slide 21
DAIDALUS Guidance Visualization:
kinematicOverview()
Interactive GUI
3D encounter visualization
DAIDALUS Track Guidance

## Slide 22
DAIDALUS Guidance Visualization:
kinematicOverview()

## Slide 23
kinematicOverview()
DAIDALUS Inputs
Encounter File
.daa
DAIDALUS Configuration
.txt
MATLAB GUI
DAIDALUS Guidance Visualization:
kinematicOverview()

## Slide 24: Goals
Generate DAIDALUS inputs
Generate DAIDALUS outputs
Visualize guidance and encounter geometry
Plot DAIDALUS outputs for in-depth analysis

## Slide 25
DAIDALUS Plots:
plotBands()
DAIDALUS Bands & Alerting Output vs. Time

## Slide 26
In-depth view of guidance throughout an encounter
Works with all 4 dimensions of DAIDALUS guidance
Alerting information overlay
DAIDALUS Plots:
plotBands()

## Slide 27
plotBands()
DAIDALUS Plots:
plotBands()
Alerts
.Time
.Ownship
.Traffic…
Units
.Time
.Ownship
.Traffic…
*Bands
.Time
.NONE
.FAR…
Aircraft trafficState
.Name
.UID…
Aircraft Performance Limits
.Alt
.Gs…

## Slide 28
DAIDALUS Plots:
plotWCV()
DAIDALUS Alerting Output vs. Time

## Slide 29
plotWCV()
DAIDALUS Plots:
plotWCV()
Alerts
.Time
.Ownship
.Traffic…
Units
.Time
.Ownship
.Traffic…

## Slide 30: Quirks & Gotcha’s
MATLAB & Java
Parallel Processing

## Slide 31: MATLAB & Java
DAIDALUS.jar must be in MATLAB’s Java Class Path to use functions that call DAIDALUS library
javaaddpath(<‘full path to DAIDALUS.jar’>) Adds jar to MATLAB class path
MATLAB will fail silently to import a jar compiled with a greater Java version than its own
MATLAB version can only be set before launch with EV “MATLAB_JAVA”
#! /bin/bash
export MATLAB_JAVA='/Library/Java/JavaVirtualMachines/jdk1.8.0_144.jdk/Contents/Home/jre’
nohup /Applications/MATLAB_R2017a.app/bin/matlab
disown -h

## Slide 32: Parallelized Functions
Some functions can take advantage of more than one processing core to speed up processing time
This requires the Parallel Computing Toolbox
Sessions without this toolbox installed, or without an active parallel pool, will run these functions on a single thread
getLVC() | 1.6x Speedup (4 Cores)
getTrafficStateIkhana() | 2.3x Speedup
getTrafficStateN3GC() | 2.4x Speedup
genScenarioTrafficState() | 3.0x Speedup

## Slide 33: BACKUP

## Slide 34: Generate DAIDALUS inputs